## Slide 1: FILTERATION OF FABRICS
NAME OF STUDENTS
Manali Kolekar -084051126
Rupesh Jadhav-084050017
Atish Mohite-084050030

## Slide 2
Filtration
Filtration means capture and retention of small particles from a moving stream either from gas or liquid , with minimum resistant to flow.
2. The fibers used in filtration fabrics are polypropylene , cotton, wool, PTFE , polyester.
INTRODUCTION

## Slide 3: Types of Filtration Operations
· Cross-flow filtration, in which a septum is
responsible for the filtering action (e.g.,
micro screens);
· Depth (or deep-bed) filtration, in which the
particles are removed throughout the filter
bed or in a significant portion of it (e.g.,
sand filters);
· Cake filtration, in which the particles are
removed on the surface of a cake formed
by the solids accumulating on a septum
(e.g., rotary vacuum filters)

## Slide 4: Classification of Filtration Systems
Filtration systems can be classified according to:
• type of operation
• direction of fluid flow with respect of filter medium
• type of filter (medium)
• flow rate or pressure control during filtration

## Slide 5
MAIN CHARACTERISTICS
1. clear filtrate
2. high capacity
3. low cake moisture content
4. long life time.
5. Porosity
6. Good flexibility

## Slide 6
There are 3 main types of filtration:
dry filtration(solid-gas)
wet filtration(solid-liquid)
gas plasma filtration
FABRIC CONSTRUCTION
Woven
Knitted
Nonwoven

## Slide 7
Fibers for dry filter manufacture are:-
Glass fibers
Standard synthetic fibers
Nomex
PET
PP
cellulosic fibers (viscose & cotton)
nylon
PTFE (Teflon),microfibers
mineral fibers
high tech fibers (e.g. PEEK), etc.

## Slide 8
Fibers For liquid filtration manufacture:-
PP, PE, PET, NYLON 11,12, polyamide, PTFE, PEEK, cotton,
Yarn is usually monofilament, multifilament, fibrillated tape or staple fiber yarn in type.
Nomex fibers are widely used for fabric filter bags.

## Slide 9: FILTER CLOTH WEAVE PATTERNS (Cloth Designs)
Plain
Twill
Satin
Leno
Basket

## Slide 10
Technologies used for manufacturing non-woven for filter fabrics -
Air laid
Electro spun
Melt blown
Needlepunch
Spun bond
Spun lace
Thermo bonded
Wetland

## Slide 11
Pretreatment processes
Calendering
Napping
Singeing
Glazing
Coating

## Slide 12
Types of Finishes given
Thermal Treatment | Chemical Treatment
Heat setting | Anti-adhesive
calendering | hydrophobe
Singeing | Oleophobe
condensing | Antistatic
 | Anti-flammable
 | Chemical resistance

## Slide 13: Tests for Filter fabrics
General QC Tests
Performance related tests .

## Slide 14: Application of filter fabrics
Geotech
Indutech
Meditech
Agrotech
Mobitech

## Slide 15
Cost of filter fabric
Type of fabric | Cost in US $
PP fabric | 1-6 per sq.m
For road construction | 0.3-0.6 per sq.m
Polyester fabric with PTFE membrane | 1.43-2.4 per sq.m
Non woven for air filters fabric | 1-10 per roll
Glass fibers filter fabric | 1-10 per piece
Stain less steel filter fabric | 1-20 per sq.m
Needle felt fabric | 2-3 per sq.m
Anti-static filter fabric | 2-20 per sq.m

## Slide 16: Market of filter fabric
Worldwide market is $6 billions in 2012
Biggest purchaser is china
Filter fabrics most used in geotech
Polyester and nylon most commonly used
Polypropylene, polyethylene, E-CTFE and PVDF respectively

## Slide 17
THANK YOU